IPIC Patent Agent Training Course

Drafting and Prosecution

Exercise # 2 – DRAFTING

Mount for Portable Machine Tools

Your “Understanding of the invention” should begin with reading the letter from the inventor and viewing of the drawings.  Ask the following questions.

1) What does the inventor call his device? Ans. a support for mounting portable tool put that in your “invention column”

2) What components does it have: plate, apertures and retainers

3) What is the function of the support for mounting portable tools? Allows several tools to be used together on a workpiece.

4) Now look a the prior art one by one. put Y if it has the component. N if not and ~ if unsure

| Invention | ‘xx5 | ‘xx8 | ‘xx1 |
| --- | --- | --- | --- |
| support for mounting portable tool | No Electric hand plane | Yes | Yes |
| a) plate | N | Y 40 | Y 10 |
| b) apertures for plural tools | N | N 24 (Single) | N 20, 22 for single tool |
| c) retainers | N | Y 26/28 | Y 32 |
| d) relieved portion | N | N | N |
| e) fence | Y | Y 70 | N |
| f) handle | Y | N | Y 15 |

5) What novel features are in the invention?

Plural tool mounting

Offset to provide continuous lateral coverage of workpiece

6) Do they relate to the function provided?  Yes, DO we need both limitations?  TO work properly, YES, but recall we are trying to have something that will work “at all”, so I would claim the polarity of tool receiving apertures in claim 1 and the fact that they are offset to provide continuous lateral coverage in Claim 2.  Now time to draft a claim.

7) Identify the elements needed to be a tool mount and add the novel element

A portable tool mount, a) a plate, b) a plurality of apertures for receiving a plurality of similar tools, c) retainers for securing each of the plurality of similar tools with respective aperture

| A portable tool mount | Keep the title simple |
| --- | --- |
| FIELD OF THE INVENTION The present application relates a portable tool mount. | Field should repeat the title and expand on it slightly if necessary. DO NOT recite specifics about the invention. |
| BACKGROUND OF THE INVENTION Portable machine tools are widely used in the construction industry. Mounts for enhancing the usefulness of portable tools are known. For example U.S. Patent No. 4,xxx,xx8 teaches a mount for a portable router that provides a tilting surface and a fence. Similarly, US Patent 5,xxx,xx1 teaches a mount for a portable router that provides a larger working surface. Portable machine tools are widely used in the construction industry. There are, however, situations in which portable tools with larger capacities than typical tools are required, but they tend to be expensive and replacement parts are not readily available. Moreover, fixed-position machine tools cannot easily be substituted for portable tools when the tools must be taken to the workplace rather than vice versa. | Set the problem to be solved by the invention. DO NOT disclose or suggest the solution provided by the invention, especially when discussing prior art. If discussing prior art a) give a complete cite, b) refer to problems in specific prior art using ‘may’. |
| SUMMARY OF THE INVENTION An object of the present invention is to provide an improved portable tool mount.. According to an aspect of the present invention there is provided <insert Claim 1 here> In an embodiment of the present invention… | One simple object statement meets utility requirement without causing any harm, and a plain-language statement of the problems addressed by the invention and the manner in which the invention overcomes these problems is helpful. Consistory clauses can merely mimic independent claims or be rewritten to be more readable. For exam something of the form shown saves time and still earns marks Support for intermediate claims can be added using devices such as “In an embodiment of the present invention”. Use phrases like “Conveniently, the means for…” |
| BRIEF DESCRIPTION OF THE DRAWINGS Embodiments of the present invention are further described with reference to the drawings in which: Fig. 1 is an upper left perspective view a portable tool mount in accordance with a first embodiment of the present invention; Fig. 2 is a lower left perspective view a portable tool mount of the embodiment of Fig. 1; Fig. 3 is a plan view of the mount of Fig. 1; Fig. 4 is a plan view a portable tool mount in accordance with a second embodiment; Fig. 5 is a plan view of mount in accordance with a third embodiment; Fig. 6 is an upper left perspective view a portable tool mount in accordance with a fourth embodiment of the present invention; | Introduce the embodiment of Fig. 1, refer the other views back to Fig. 1. |
| DETAILED DESCRIPTION | Provide a top down description logical description of what the invention is then how it works. Use reference characters to refer to figures. |
| CLAIMS What is claimed is: 1. A portable tool mount comprising: a plate; a plurality of apertures in space relation in the plate for receiving similar portable tools; and retainers associated with each of the plurality of apertures for securing respective tools to the plate. | Independent Claims are a single sentence, when read with the introduction “What is claimed is:” Recite only essential elements. Recite each element positively, not as part of another element. Consider and independent claim for each category, apparatus method and product. Certain technologies have specialized types of claims, for example “Use claims” in place of methods of medical treatment. Do not use “use claims” for other technologies as use is covered by “make , use and sell” |
| Dependent claims 2. The portable tool mount as claimed in claim 1 wherein the plurality of apertures are arranged for contiguous lateral coverage by the plurality of portable tools. 3. The portable tool mount as claimed in claim 2 wherein the plurality of apertures are offset longitudinally. 4. The portable tool mount as claimed in claim 3 wherein the plurality of apertures overlap laterally. 5. The portable tool mount as claimed in claim 1 wherein each aperture has relieved portion associated therewith. Etc. For fence, handle and so on | Recite further detail ONLY put one limitation in per dependent claim UNLESS they are cooperative features that cannot stand alone; |
| ABSTRACT OF THE DISCLOSURE The portable tool mount allows a plurality of similar portal tools to be secured in a ganged array to provide a larger tool working width. The mount includes a plate and a plurality of apertures for receiving a plurality of portable tools. Each aperture has a retainer associated with it to secure the portable tool to the plate. For example, two or more portable planers can be mount to provide nearly twice the planer width of a single planer. Similarly two or more sanders can be mounted to cover a larger working surface. | The abstract should be specific and be to the disclosure as a whole. Should not merely copy claim 1. Avoid claim language such as means and said, run-on sentences etc. Avoid words like “improved” Make the abstract readable, it is intended for searching and is not supposed to be used to limit the scope of the claims. Keep it brief, maximum 150 for PCT. |